## Slide 1: Engineering Economics ECO 1192 Lecture 6: Cost-Benefit Analysis (CBA)
Claude Théoret
University of Ottawa

## Slide 2: Recommended Readings
Fraser et al.* chapter 10
  Newnan et al. chapter 16

## Slide 3: Lecture Content
Cost-Benefit Analysis (CBA)
  Major Steps of CBA
  Benefits and costs included?
  Decision Rules
    CBA and Independent Projects
    CBA and Mutually Exclusive Projects

## Slide 4: What is Cost-Benefit Analysis (CBA)?
Policy/program/project assessment method that quantifies the value of policy consequences (usually called impacts) in monetary terms to all members of society
  calculates net social benefits (social benefits minus social costs) for each policy alternative
Tool for helping to make public decisions—what programs and policies to introduce—done from the standpoint of society rather than from that of a single profit-making firm
Methods and techniques for evaluating the social consequences of economic phenomena, policies and projects.
Systematic methodology for measuring the benefits and costs of government programs to the population.

## Slide 5: Private CBA: Major Steps
Essentially four steps:
Identify the set of possible projects to be considered (i.e., list the major alternatives).
Identify the full consequences of each alternative (i.e., inputs and outputs).
Assign a value to each input and output (i.e., estimate the costs e.g., inputs and the prices of outputs).
Add the costs and benefits to estimate the total profitability of the project
  i.e., maximize profitability.

## Slide 6: Treasury Board Guidelines for Public Projects: Major Steps
1. Examine needs, consider constraints, and formulate objectives and targets. State the point of view from which costs and benefits will be assessed.
2. Define options in a way that enables the analyst to compare them fairly. If one option is being assessed against a base case, ensure that the base case is optimised.
3. Analyze incremental effects and gather data about costs and benefits. Set out the costs and benefits over time in a spreadsheet.
4. Express the cost and benefit data in a valid standard unit of measurement (for example, convert nominal dollars to constant dollars, and use accurate, undistorted prices).
5. Run the deterministic model (using single-value costs and benefits as though the values were certain). See what the deterministic estimate of net present value (NPV) is.

## Slide 7: Treasury Board Guidelines for Public Projects: Major Steps (cont’d)
6. Conduct a sensitivity analysis to determine which variables appear to have the most influence on the NPV. Consider whether better information about the values of these variables could be obtained to limit the uncertainty, or whether action can limit the uncertainty.
7. Analyse risk by using what is known about the ranges and probabilities of the costs and benefits values and by simulating expected outcomes of the investment. What is the expected net present value (ENPV)? Apply the standard decision rules.
8. Identify the option, which gives the desirable distribution of income (by income class, gender or region - whatever categorisation is appropriate).
9. Considering all of the quantitative analysis, as well as the qualitative analysis of factors that cannot be expressed in dollars, make a reasoned recommendation.

## Slide 8: Private and Public CBA: Major Differences
Private sector
  single objective: profitability
Governments face multiple objectives
  social, economic, cultural, ecological
Firms rely exclusively on market prices to evaluate inputs and outputs.
Governments cannot rely exclusively on market prices because
  Market prices may not exist
    clean air, lives saved, time saved
  Market failure can distort prices
    Market demand and supply curves do not truly reflect the value of a good and its production cost respectively

## Slide 9: Ferry: Major Link Between Two Cities
Privately owned
$3 per passenger
Average operating cost: $1.50
Income tax rate: 30%.
300,000 passengers annually
Non operating costs per passenger
  Carbon monoxide fumes = $0.10
  Water pollution = $0.05
  Noise pollution = $0.02
  Sea sickness = $0.05
Average crossing time = 60 minutes
Major accidents per year
  Accidental deaths = 1
  Lost workdays due to injuries = 100.

## Slide 10: Conventional Benefit-Cost Ratio (CBR)
1. Present Worth Measure
PW (Project Benefits) ÷ [PW of Project Costs - PW of Salvage value]
2. Future Worth Measure
= FW (Project Benefits) ÷ [FW of Project Costs - Salvage value]
3. Annual Equivalent Worth
AEW (Project Benefits) ÷ [AEW of Project Costs - AEW of Salvage value]
Note that, in the conventional approach to B/C ratios, a project’s positive salvage value (SV) offsets operating costs (and is added to operating costs if < $0).

## Slide 11: Modified Benefit-Cost Ratio (MCBR)
1. Present Worth Measure
PW (Benefits - O+M Expenses) ÷ [PW of Initial Cost - PW of Salvage value]
O+M = Operating and maintenance
2. Future Worth Measure
FW (Benefits – O+M Expenses) ÷ [FW of Initial Cost – FW of Salvage value]
3. Annual Equivalent Worth
AEW (Benefits – O+M Expenses) ÷ [AEW of Initial Cost - AEW of Salvage value]
Note that, in the conventional approach to B/C ratios, a project’s positive salvage value (SV) offsets operating costs (and is added to operating costs if < $0).

## Slide 12: Summary Table: B/C Ratio
 | TYPES OF PROJECTS | 
 | MUTUALLY EXCLUSIVE PROJECTS | INDEPENDENT PROJECTS
APPROACH | INCREMENTAL B/C RATIO (Must be applied only after determining that at least one project has a valid B÷C ratio) | Select all projects (no capital rationing) with acceptable B÷C ratios.
Decision Threshold : B÷C or ∆B÷∆C = 1 |  | 
DECISION CRITERIA | Select the better project after exhausting all pair-wise project comparisons. | B÷C ≥ 1

## Slide 13: Incremental B/C ratios: Warning !!!!
The PW, FW and annuity methods can be used to calculate
  individual B/C ratios (independent projects)
  incremental B/C ratios (mutually exclusive projects).
If the projects are mutually exclusive and have different lives, you will be required to repeat projects of unequal durations if using the PW and FW methods.
Repeating projects will require to adjust their initial investment.
To avoid this problem, always use the annuity approach to calculate the incremental B/C ratios of projects with different lives.
?
?
?
?
?
?

## Slide 14: CBA Steps for Mutually Exclusive Projects
1. Rank projects in ascending order of first or initial costs
2. Ensure that at least one project (any one) has an individual B/C ratio at least equal to one
3. Using the incremental B/C method, compare the two smallest projects
4. Use the following rule to decide on the better of two projects: assuming that the B/C ratio exceeds one, take the larger (the one with larger initial cost) project; if smaller than one, take the smaller project.
5. Exhaust all pair-wise comparisons using the incremental B/C method.
6. The last project to be retained is the best project among mutually exclusive projects.

## Slide 15: Conventional BCR and ∆B∆C Ratios
For independent projects, the B/C ratio leads to the same selection of acceptable projects as the NPW, NFW, IRR and ERR methods (no capital budgeting).
For mutually exclusive projects, the B/C ratio leads to selection of the same best project as the NPW (same period of analysis), NFW (same period of analysis), and incremental IRR and ERR methods.

## Slide 16: Example Mutually Exclusive Projects
Project | First Cost | Annual Benefits | Power Sales | Annual Operating Costs
A | 25,000 | 1,700 | 1,500 | 200
B | 35,000 | 2,000 | 1,800 | 250
C | 50,000 | 2,450 | 3,600 | 350
Creek County is examining three alternative plans for a new road into a marsh. These mutually exclusive plans have different costs and benefits as indicated in the following table ($K).
Each road has an economic life of 50 years, and MARR = 10%.

## Slide 17: Questions
1. Which projects are acceptable?
3. Which project is better (best)?

## Slide 18: B/C ratios for projects A, B and C
Project A
(B/C) = [1700+1,500] ÷ [25,000(A/P,10%,50)+ 200]
= (3,200 ÷ 2,721.5) = 1.18 > 1: valid project
Project B
(B/C) = [2,000+1,800] ÷ [35,000(A/P,10%,50)+ 250]
= (3,800 ÷ 3,780.1) = 1.005 > 1: valid project
Project C
(B/C) = [3,600+2,450] ÷ [50,000(A/P,10%,50)+ 350]
= (6,050 ÷ 5,393) = 1.12 > 1: valid project

## Slide 19: Acceptable Independent Projects?
In the absence of capital rationing (i.e., the potential investor has sufficient funds to develop the three projects), select projects A, B and C

## Slide 20: Determine the incremental B/C ratio between projects A and B
The incremental B/C ratio between projects A & B is (∆B/∆C)
= (3800 – 3200) ÷ (3780.1 – 2721.5)
= 2850 ÷ 2671.5
= 0.57 < 1
Decision: Select project A (i.e., the smaller project)

## Slide 21: Determine the incremental B/C ratio between projects A and C
The incremental B/C ratio between projects C & A is (∆B/∆C)
= (6050 – 3200) ÷ (5393 – 2721.5)
= 2850 ÷ 2671.5
= 1.07 > 1
Decision: Select project C (i.e., the larger project) even though Project A has the largest individual B/C ratio (= 1.18)

## Slide 22: Summary Information
Project | First Cost | Annual Benefit | Power Sales | Annual Costs
A | 25,000 | 1,700 | 1,500 | 200
B | 35,000 | 2,000 | 1,800 | 250
C | 50,000 | 2,450 | 3,600 | 350
B/C RATIOS (%) A B C |  |  | 
A | 1.18 | 0.57 | 1.07
B | 0.57 | 1.01 | ?
C | 1.07 | ? | 1.12

## Slide 23: Which project is best?
Based on the incremental method for mutually exclusive projects, Project C is the best project.

## Slide 24: Example
Project | FIRST COST (M$) | Individual B/C Ratio | INCREMENTAL B/C RATIOS A B C D |  |  | 
A | 10 | 1.6 |  |  |  | 
B | 15 | 2.7 | 1.5 (B) |  |  | 
C | 20 | 1.7 | 0.9 | 1.2 (C) |  | 
D | 29 | 1.3 | 1.1 | 0.9 | 1.3 (D) | 
E | 35 | 1.1 | 0.8 | 0.5 | 0.8 | 0.9

## Slide 25: Decision for independent projects?
If A, B, C, D and E are independent
(without capital rationing), select all
projects (all B/C ratios > 1)

## Slide 26: Decision for mutually exclusive projects?
If A, B, C, D and E are mutually
exclusive projects, select project D.

## Slide 27: Summary Measures: A Comparison
Single sums (PW and FW), annual equivalent (AEW) and ERR methods require fewer calculations than IRR methods
In some cases,
  Decision-makers may be more familiar with annual equivalent analysis  easier to explain
  A rate of return method may be easier to explain to people unfamiliar with economic analysis
Generally, businesses favour one method over others for a variety of reasons
  History (been done this way by the corporation for years)
  Background (training …)
  Familiarity with competing techniques

## Slide 28: Summary Measures: A Comparison (cont’d)
Single Sum (Present & Future Worth)
Gives explicit measure of a project’s profit contribution
Makes it difficult to compare projects of different sizes and durations
Annual Worth (AEW)
Familiarity with cash flow concepts makes interpretation of results easier
Underlying assumption makes the comparison of projects of different sizes more tenuous/questionable

## Slide 29: Summary Measures: A Comparison (cont’d)
IRR
Makes it easier to compare projects of different sizes
Can be difficult to calculate
  indirect method
  multiple IRRs (some negative)

## Slide 30: Summary Measures: A Comparison (cont’d)
Payback Period
Easy to calculate; widespread use
Focus on liquidity; other methods focus on profitability
Discriminates against long-term projects
  Ignores a project’s expected service life
Ignores time-value mechanics (simple payback)

## Slide 31: Next Lecture
      Depreciation
      Taxes
      Cash Flows

## Slide 32: Engineering Economics ECO 1192 Lecture 6: Cost-Benefit Analysis (CBA)
Claude Théoret
University of Ottawa